## Slide 1: Pathology Introduction
By
Prof. Dr. SALAH FAYED

## Slide 2: Introduction
Pathology is the scientific study of diseases.
Importance of Pathology:
  Pathology is a clinical knowledge service that is fundamental to modern medical practice.
  It is used in the diagnosis, treatment and management of many clinical conditions.

## Slide 3: Introduction
Objectives of studying pathology:
  Definition of pathology.
  Description and explanation of cell injury and cellular adaptation.
  Description & comparison between acute and chronic inflammation.
  Discussion of tissue repair.
  Discussion of some infective diseases as T B, Syphilis, leprosy, schistosomiasis, & malaria.

## Slide 4: Introduction
  Identification of circulatory disturbances as edema, thrombosis, embolism infarction, hemorrhage and shock.
  Definition of neoplasia, comparison between benign and malignant tumors, identification of the etiology of the tumors, and description of some common tumors.
  Identification of pathologic lesions, specific for each system of the body, (cardiovascular, respiratory, digestive, urinary, reproductive, ……)

## Slide 5: Introduction
What is the disease?
  It is an abnormal variation of the structure and function of any organ or tissue of the body.

## Slide 6: Introduction
Study of a disease include the following items:
Definition.
Etiology (predisposing factors, causes).
Pathogenesis ( mechanisms that lead to production of the disease).
Morphologic changes (gross and microscopic changes).

## Slide 7: Introduction
Clinical features (symptoms and signs).
Fate (end results of the disease).
Complications the bad effects of the disease.
Prognosis (forecast of the probable course or outcome of a disease).

## Slide 8: Introduction
Classification of diseases:
Congenital:
  The patient is born with the disease (due to genetic abnormality or an acquired injury in utero).
Acquired:
  Have no genetic basis.

## Slide 9: Introduction
The study of pathology is divided into:
General pathology (introductory):
  Concerned with the study of basic reactions of cells and tissues to abnormal stimuli.
Systematic pathology:
  Concerned with the study of specific responses of specialized organs and tissues to well defined stimuli.

## Slide 10: Introduction
Techniques that used in pathology:
Tissue processing:
  The biopsies taken from the patients for diagnosis of diseases, must be processed in the pathology laboratory to produce microscopic slides that are viewed under the microscope by pathologists.

## Slide 11: Introduction
Specimen recording:
  Every specimen received in the surgical pathology laboratory must be accompanied by a request containing the patient information, disease history, and the site of the biopsy.
  The specimens are recorded by giving them a number that will identify each specimen for each patient.

## Slide 12: Introduction
Gross examination and trimming:
  The specimens arrived to Pathology Department must be examined by the pathologist by the naked eye (gross examination) including:
    Description of the specimen.
    Choosing parts of it for processing (trimming).

## Slide 13: Gross examination of the specimen & Trimming

## Slide 14: Introduction
Fixation of the tissues:
  It must be carried out as soon as possible after removal of the tissues form the body to prevent autolysis.
  There is a variety of fixatives, the use of each is depending on the type of tissue present and the features to be demonstrated.

## Slide 15: Introduction
    Fixatives:
      Formalin: is used for all routine surgical pathology and autopsy tissues.
  Zenker’s fixatives are recommended for lymph nodes, spleen, thymus and bone marrow. The solution fixes the nuclei very well and gives good detail.

## Slide 16: Introduction
  Glutaraldhyde is recommended for fixation of tissues for electron microscopy.
  Alcohols , specifically ethanol (95%) are used for cytologic smears and frozen sections.
  Bouin’s solution is recommended for fixation of testis, GIT, and endocrine tissue.

## Slide 17: Introduction
Tissue processing:
  Once the tissue has been fixed, it must be processed into a form in which it can be made into thin microscopic sections.
  Tissues are treated as follows:
    First, the water in the tissues must be removed by dehydration. This is usually done with a series of alcohols (70%, 95%, 100%)

## Slide 18: Introduction
    The next step is called “clearing” and consists of removal of dehydrant with a substance that will be miscible with the embedding medium (paraffin wax). The commonest clearing agent is xylene.
    Finally, the tissues are infiltrated with the embedding agent (paraffin wax). Paraffin waxes have different melting point for various hardness.

## Slide 19: Introduction
  The already mentioned processes are automated for the large volumes of routine tissues processed.
  The “Technicon” tissue processor is commonly used for this purpose.

## Slide 20: Tissue processor (Technicon)

## Slide 21: Introduction
Tissue blocking:
  Tissues that come off the tissue processor must be manually put into blocks by the technician who must pick the tissues out of the cassette and pour molten paraffin over them.
  After hardening of the block, it will be ready for cutting by the microtome.

## Slide 22: Tissue blocking

## Slide 23: Introduction
Sectioning (tissue cutting):
  The tissues must be cut into very thin sections that can be placed on a slide. This done by a microtome.
  Microtome is an apparatus containing a knife holder with a mechanism for advancing a paraffin block standard distance across it.

## Slide 24: The microtome

## Slide 25: Introduction
  The knives used in cutting are either of the standard thick metal variety or thin disposable variety. The latter is commonly used now.
  Sectioning of tissues is a real art and takes much skill and practice.

## Slide 26: Introduction
  Once sections are cut, they are floated on a warm water bath (temp is 56° C) that remove wrinkles.
  Then they are picked up on a glass microscopic slides.
  The slides are put on a hot plate (about 58° C) for fixation of tissues on the slides.

## Slide 27: Tissue floating bath

## Slide 28: Paraffin section on a slide

## Slide 29: Hot plate for slides

## Slide 30: Introduction
Frozen sections:
  Used for rapid diagnosis of a pathologic condition.
  For example, the surgeon may want to know if the mass is benign or malignant while he is in the operation theater.
  The tissues to be studied are frozen in a cold liquid or cold environment ( -20° C to -30° C).
  This is performed by an apparatus called “Cryostat”.

## Slide 31: Cryostat

## Slide 32: Introduction
Staining of tissues:
  The paraffin wax in the tissue sections must be removed to allow staining by water soluble dyes.
  So, deparaffinization by xylene and rehydration by descending grades of alcohols will be done.
  There are many stains for the tissue, but the routine stain used is hematoxylin and eosin (H & E). Usually automated stainer is used.
  Other stains are used in specific situations according to the diagnostic needs.

## Slide 33: Automated stainer

## Slide 34: Introduction
Covering of the stained tissue:
  Thin glass cover is used.
  DPX is used for adhesion of the cover.

## Slide 35: Cover slipping

## Slide 36: Introduction
Results of staining by H & E:
  Nuclei and other basophilic structures are blue.
  Cytoplasm and acidophilic structures are red.

## Slide 37: Examples of H & E sections

## Slide 38: References
Essential reference:
  Robbin’s basic pathology by Kumar and others.
Recommended books:
  General and systemic pathology by Underwood.
  Robbin’s and Cotran pathologic basis of disease.
Web sites:
  Web path, the internet pathology laboratory.